## Slide 1
8D Problem-Solving
Facilitator Teaching Guide | Root Cause Analysis & Corrective Action
D0
ERA
D1
Team
D2
Problem
D3
ICA
D4
RCA
D5
PCA
D6
Implement
D7
Prevent
D8
Close
WHAT IS 8D?
A structured 8-step methodology to identify, correct, and prevent recurring defects. Each discipline builds on the previous — from emergency containment through to permanent prevention and team recognition.
KEY TOOLS INSIDE
• Is / Is-Not Problem Definition • Fishbone (Ishikawa) Diagram • 5-Why Logic Tree • ICA → PCA Action Templates • Corrective Action Tracker
HOW TO USE
Follow slides D0 → D8 in sequence. Each slide is a fill-in template for your team. Use the Tracker (slide 10) to assign owners and due dates, and the Quick Ref card (slide 11) as a pocket reminder.
Based on Ford 8D Methodology | For Training & Workshop Use

## Slide 2
D1 — Establish the Problem Solving Team
Cross-functional team with knowledge, time, authority and skills to solve the problem
Champion / Sponsor
Executive authority to approve resources
Removes organizational barriers
Reviews progress at milestones
Approves 8D report sign-off
Team Leader
Owns 8D process & timeline
Facilitates meetings & workshops
Communicates with customer
Ensures SMART actions assigned
Core Members
Engineering, Quality, Manufacturing
Process or system owner
Supplier rep (if applicable)
Min. 3, Max. 6 recommended
TEAM CHARTER TEMPLATE
Team Name: _________________
Problem Statement (brief): _________________
Champion: _________________
Team Leader: _________________
Core Members: _________________
Target Completion Date: _________________
Meeting Cadence: _________________
Success Criteria: _________________

## Slide 3
D2 — Problem Description
Use the IS / IS NOT method to describe the problem quantitatively and precisely
DIMENSION
IS (What IS known)
IS NOT (What is NOT the case)
DISTINCTION
WHAT
Dimension out of spec on Part #A123
All other dimensions — only OD affected
Only one feature is non-conforming
WHERE
Press Shop, Machine #4, Station 3
Other machines or stations
Localized to one asset — machine-specific
WHEN
Shift B, after tool change on 2024-01-15
Before tool change or other shifts
Timing correlates with tool replacement
EXTENT
18% defect rate — 540 of 3,000 parts
100% of production — not systemic
Partial — suggests intermittent cause
PROBLEM STATEMENT
"Since 2024-01-15 on Machine #4 Station 3, the OD of Part #A123 is out of spec at 18% defect rate. No other parts or machines are affected."
5W2H CHECKLIST — COMPLETE BEFORE WRITING STATEMENT
Who: Who discovered? Who is affected?
What: What is the defect? What should it be?
Where: Where on the part? Where in the process?
When: When did it start? How often?
Why: Why is it a problem? (impact)
How: How was it found? Inspection/test method?
How Much: Quantity, rate, cost, risk?

## Slide 4
D3 — Interim Containment Action (ICA)
Band-aid fix to PROTECT the customer while root cause investigation is ongoing
KEY PRINCIPLE: ICA is NOT the permanent fix — it buys time. Remove ICA only after PCA is verified effective.
COMMON ICA METHODS
100% inspection / sorting of suspect product
Quarantine in-process and finished goods
Recall / sort at customer / field location
Temporary design or process deviation
Additional inspection checkpoint added
Supplier source inspection increased
Customer notification & stock audit
Expedited replacement shipment
ICA DOCUMENTATION TEMPLATE
ICA Action Taken: ________________________
Owner: ________________________
Start Date: ________________________
Target Remove Date: ________________________
Effectiveness Measure: ________________________
Verification Method: ________________________
Customer Notification (Y/N): ___
Stock Qty Quarantined: ________________________
ICA VERIFICATION CHECKLIST: ☐ Customer confirmed protected ☐ Zero new escapes since ICA ☐ Defect rate at customer = 0 ☐ ICA removal plan documented ☐ ICA owner assigned

## Slide 5
D4 — Fishbone (Ishikawa) Diagram — 6M Root Cause Analysis
MAN
▸ Untrained operator ▸ Fatigue / distraction ▸ No standard work ▸ High turnover
MACHINE
▸ Tool worn past interval ▸ Machine vibration ▸ No prev. maintenance ▸ Sensor out of cal.
METHOD
▸ No process docs ▸ Wrong setup procedure ▸ Unclear cycle time ▸ Vague inspection method
MATERIAL
▸ Incoming material OOS ▸ Wrong material grade ▸ Moisture / contamination ▸ Supplier variation
MEASUREMENT
▸ No Gauge R&R done ▸ Wrong gauge used ▸ Measurement bias ▸ Data entry errors
ENVIRONMENT
▸ Temperature variation ▸ Humidity / dust ▸ Vibration from machinery ▸ Inadequate lighting
EFFECT (Problem Statement Here)
INSTRUCTIONS: Brainstorm all possible causes for each category. Circle the top 3. Each becomes a 5-Why investigation (see next slide).

## Slide 6
D4 — Root Cause Analysis: 5-Why Logic Tree
Ask "Why?" 5 times to reach root cause · Map Occurrence RC / Escape RC / Systemic RC
WHY 1
Why did the part OD go out of spec?
The cutting tool was worn beyond its replacement interval.
WHY 2
Why was the cutting tool worn beyond interval?
The tool change schedule was not followed by the operator.
WHY 3
Why was the tool change schedule not followed?
The PM alert on the HMI was disabled by maintenance.
WHY 4
Why was the HMI PM alert disabled?
No procedure exists to prevent disabling preventive alerts.
WHY 5
Why does no procedure exist for this?
★ ROOT CAUSE: Change control system does not cover HMI parameter changes.
STEP QUESTION (Why?) ANSWER / FINDING
3 Root Cause Types: Occurrence (why it happened) · Escape (why not caught) · Systemic (why system allowed it)

## Slide 7
D5 & D6 — Choose, Verify & Implement Corrective Actions
D5: Select best PCA from alternatives | D6: Implement PCA & confirm ICA can be removed
D5 — SELECT PERMANENT CORRECTIVE ACTION
PCA must address ROOT cause, not symptom
Test alternatives before selecting — use trial / pilot
Verify PCA does not cause new problems
Use decision matrix if multiple options exist
Get management & customer approval if required
Confirm ICA effectiveness data supports removal
DECISION MATRIX — RATE 1-5
OPTION
Effectiveness
Feasibility
Cost
Speed
TOTAL
Option A: Replace tool on fixed interval
5
4
3
4
16
Option B: Add sensor for real-time wear
4
3
2
2
11
Option C: Update PM system procedure
3
5
5
5
18
D6 — IMPLEMENT & VALIDATE PCA
Step 1 Update process documentation (PFMEA, Control Plan, SOP)
Step 2 Conduct operator training on new standard
Step 3 Implement changes in full production run
Step 4 Collect data to verify defect rate = 0 over defined period
Step 5 Confirm ICA can be removed — document removal date
Step 6 Customer confirms satisfaction — get written approval
VALIDATION EVIDENCE REQUIRED
SPC charts | PPM data | Gauge R&R | Customer scorecard | Audit results | Production trial report

## Slide 8
D7 — Prevent Recurrence (Systemic Fix)
Update ALL systems to prevent this failure from EVER happening again — at this and similar processes
PROCESS DOCUMENTS
Update PFMEA — add new failure mode
Revise Control Plan with new controls
Update Work Instructions / SOPs
Update Process Flow Diagram
Update PPAP submission if applicable
SYSTEMS & TECHNOLOGY
Update CMMS / preventive maint. records
Add new PM task to schedule
Update HMI parameter change procedure
Install poka-yoke or error-proofing device
Update alarm & alert configurations
PEOPLE & TRAINING
Retrain all operators on new SOP
Update training matrix records
Brief supervisors and management
Update new-hire onboarding content
Document lessons learned in LMS
HORIZONTAL DEPLOYMENT
Identify similar processes / products
Apply fix to all analogous operations
Notify sister plants / divisions
Update corporate quality standards
Add to lessons-learned database
LESSONS LEARNED ENTRY: Part/System: _____ | Root Cause Summary: _____ | Fix Applied: _____ | Other Products at Risk: _____ | Knowledge Owner: _____

## Slide 9
D8 — Recognize the Team & Close the 8D
Acknowledge contributions | Formally close the 8D | Archive for lessons learned database
CLOSURE GATE CHECKLIST
☐ D0: ERA documented and effective
☐ D1: Team charter signed
☐ D2: Problem statement agreed by customer
☐ D3: ICA verified; removal date confirmed
☐ D4: Root causes validated with data
☐ D5: PCA selected — decision documented
☐ D6: PCA implemented; zero new defects
☐ D7: All documents updated; training done
☐ D8: Team recognized; report signed off
☐ Customer written acceptance received
TEAM RECOGNITION TEMPLATE
8D Title / Problem: _________________________
Team Leader: _________________________
Core Members: _________________________
Problem Solved Date: _________________________
Customer Impact Avoided: _________________________
Cost Savings Achieved: _________________________
Key Lesson Learned: _________________________
Signed (Champion): _________________________
Date Closed: _________________________

## Slide 10
8D Corrective Action Tracker
8D #: _______ Part: _______ Customer: _______ Open Date: _______ Target Close: _______ Status: IN PROGRESS
Stage | D-Step Action | Owner | Due | Status | Evidence / Link
D0 ERA | Notify customer + quarantine suspect stock | J. Smith | Jan 16 | DONE | Email #1023
D1 Team | Assemble team + sign charter | K. Lee | Jan 17 | DONE | Charter v1.0
D2 Prob. | IS/IS NOT + problem statement | K. Lee | Jan 19 | DONE | D2 Worksheet
D3 Cont. | 100% sort at customer + station inspection | M. Wong | Jan 20 | DONE | Sort Rpt #42
D4 RCA | Fishbone + 5-Why; validate root causes | Team | Jan 26 | DONE | D4 Analysis
D5 Select | Decision matrix; approve Option C PCA | K. Lee | Jan 30 | DONE | Dec. Matrix
D6 Impl. | Update PM procedure; pilot run; validate | R. Patel | Feb 10 | IN PROG | 
D7 Prevent | Update PFMEA, CP, SOP; training records | Q. Team | Feb 20 | PENDING | 
D8 Close | Team recognition; champion sign-off; archive | K. Lee | Feb 25 | PENDING | 
Status: DONE = verified · IN PROG = in progress · PENDING = not started · OVERDUE = past due

## Slide 11
8D Quick Reference Card | D0 through D8 at a glance
D0 — Emergency Response
Timing: Within 24h Key Tool: Sort / Quarantine Output: ERA documented
D1 — Problem Solving Team
Timing: Day 1-2 Key Tool: Team Charter Output: Signed charter
D2 — Problem Description
Timing: Day 2-3 Key Tool: IS/IS NOT + 5W2H Output: Problem statement
D3 — Interim Containment
Timing: Day 2-5 Key Tool: Sort / 100% Inspect Output: ICA verified
D4 — Root Cause Analysis
Timing: Week 1-2 Key Tool: Fishbone + 5-Why Output: RC validated
D5 — Select PCA
Timing: Week 2 Key Tool: Decision Matrix Output: PCA approved
D6 — Implement & Validate
Timing: Week 2-4 Key Tool: PFMEA / SPC Data Output: Defect rate = 0
D7 — Prevent Recurrence
Timing: Week 3-5 Key Tool: PFMEA / CP / SOP Output: Docs updated
D8 — Recognize & Close
Timing: Week 4-6 Key Tool: 8D Report Sign-off Output: 8D closed
Refer to individual D-stage slides for full templates, tools, and worked examples.